## Slide 1
Chapter 1
Digital Design and Computer Architecture: ARM® Edition
Sarah L. Harris and David Money Harris

## Slide 2
Two discrete values:
  1’s and 0’s
  1, TRUE, HIGH
  0, FALSE, LOW
1 and 0: voltage levels, rotating gears, fluid levels, etc.
Digital circuits use voltage levels to represent 1 and 0
Bit: Binary digit
Digital Discipline: Binary Values

## Slide 3
Decimal numbers
Binary numbers
Number Systems

## Slide 4
20 = 1
21 = 2
22 = 4
23 = 8
24 = 16
25 = 32
26 = 64
27 = 128
28 = 256
29 = 512
210 = 1024
211 = 2048
212 = 4096
213 = 8192
214 = 16384
215 = 32768
Powers of Two
Handy to memorize

## Slide 5
Binary to decimal conversion:
  Convert 100112 to decimal
  16×1 + 8×0 + 4×0 + 2×1 + 1×1 = 1910
Decimal to binary conversion:
  Convert 4710 to binary
  32×1 + 16×0 + 8×1 + 4×1 + 2×1 + 1×1 = 1011112
Number Conversion

## Slide 6
Two methods:
  Method 1: Find the largest power of 2 that fits, subtract and repeat
  Method 2: Repeatedly divide by 2, remainder goes in next most significant bit
Decimal to Binary Conversion

## Slide 7
  5310
  Method 1: Find the largest power of 2 that fits, subtract and repeat
  5310 32×1
  53-32 = 21 16×1
  21-16 = 5 4×1
  5-4 = 1 1×1 = 1101012
Method 2: Repeatedly divide by 2, remainder goes in next most significant bit
  5310 = 53/2 = 26 R1
  26/2 = 13 R0
  13/2 = 6 R1
  6/2 = 3 R0
  3/2 = 1 R1
  1/2 = 0 R1 = 1101012
Decimal to Binary Conversion

## Slide 8
  Another example: Convert 7510 to binary.
  7510= 64 + 8 + 2 + 1 = 10010112
or
75/2 = 37 R1
37/2 = 18 R1
18/2 = 9 R0
9/2 = 4 R1
4/2 = 2 R0
2/2 = 1 R0
1/2 = 0 R1
Decimal to Binary Conversion

## Slide 9
N-digit decimal number
  How many values? 10N
  Range? [0, 10N - 1]
  Example: 3-digit decimal number:
    103 = 1000 possible values
    Range: [0, 999]
N-bit binary number
  How many values? 2N
  Range: [0, 2N - 1]
  Example: 3-digit binary number:
    23 = 8 possible values
    Range: [0, 7] = [0002 to 1112]
Binary Values and Range

## Slide 10
Hexadecimal Numbers
Hex Digit | Decimal Equivalent | Binary Equivalent
0 | 0 | 0000
1 | 1 | 0001
2 | 2 | 0010
3 | 3 | 0011
4 | 4 | 0100
5 | 5 | 0101
6 | 6 | 0110
7 | 7 | 0111
8 | 8 | 1000
9 | 9 | 1001
A | 10 | 1010
B | 11 | 1011
C | 12 | 1100
D | 13 | 1101
E | 14 | 1110
F | 15 | 1111

## Slide 11
Base 16
Shorthand for binary
Hexadecimal Numbers

## Slide 12
Hexadecimal to binary conversion:
  Convert 4AF16 (also written 0x4AF) to binary
  0100 1010 11112
Hexadecimal to decimal conversion:
  Convert 4AF16 to decimal
  162×4 + 161×10 + 160×15 = 119910
Hexadecimal to Binary Conversion

## Slide 13
Bits
Bytes & Nibbles
Bytes
Bits, Bytes, Nibbles…

## Slide 14
210 = 1 kilo ≈ 1000 (1024)
220 = 1 mega ≈ 1 million (1,048,576)
230 = 1 giga ≈ 1 billion (1,073,741,824)
Large Powers of Two

## Slide 15
210 = 1 kilo ≈ 1000 (1024)
220 = 1 mega ≈ 1 million (1,048,576)
230 = 1 giga ≈ 1 billion (1,073,741,824)
Large Powers of Two
 | x= | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
 | 2**x | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512
(K) | 2**1x |  |  |  |  |  |  |  |  |  | 
(M) | 2**2x |  |  |  |  |  |  |  |  |  | 
(G) | 2**3x |  |  |  |  |  |  |  |  |  | 
(T) | 2**4x |  |  |  |  |  |  |  |  |  | 
(P) | 2**5x |  |  |  |  |  |  |  |  |  | 
(E) | 2**6x |  |  |  |  |  |  |  |  |  | 

## Slide 16
What is the value of 224?
24 × 220 ≈ 16 million
How many values can a 32-bit variable represent?
22 × 230 ≈ 4 billion
Estimating Powers of Two

## Slide 17
Decimal
Binary
Addition

## Slide 18
Add the following 4-bit binary numbers
Add the following 4-bit binary numbers
Binary Addition Examples

## Slide 19
Digital systems operate on a fixed number of bits
Overflow: when result is too big to fit in the available number of bits
See previous example of 11 + 6
Overflow

## Slide 20
Sign/Magnitude Numbers
Two’s Complement Numbers
Signed Binary Numbers

## Slide 21
1 sign bit, N-1 magnitude bits
Sign bit is the most significant (left-most) bit
  Positive number: sign bit = 0
  Negative number: sign bit = 1
Example, 4-bit sign/mag representations of ± 6:
+6 = 0110
- 6 = 1110
Range of an N-bit sign/magnitude number:
[-(2N-1-1), 2N-1-1]
Sign/Magnitude Numbers

## Slide 22
Problems:
Addition doesn’t work, for example -6 + 6:
1110
+ 0110
10100 (wrong!)
Two representations of 0 (± 0):
1000
0000
Sign/Magnitude Numbers

## Slide 23
Don’t have same problems as sign/magnitude numbers:
  Addition works
  Single representation for 0
Two’s Complement Numbers

## Slide 24
msb has value of -2N-1
Most positive 4-bit number: 0111
Most negative 4-bit number: 1000
The most significant bit still indicates the sign (1 = negative, 0 = positive)
  Range of an N-bit two’s complement number:
  [-(2N-1), 2N-1-1]
Two’s Complement Numbers
+

## Slide 25
“Taking the Two’s complement” flips the sign of a two’s complement number
Method:
    Invert the bits
    Add 1
Example: Flip the sign of 310 = 00112
    1100
    + 1
    1101 = -310
“Taking the Two’s Complement”

## Slide 26
Take the two’s complement of 610 = 01102
    1001
    + 1
    10102 = -610
What is the decimal value of the two’s complement number 10012?
    0110
    + 1
    01112 = 710, so 10012 = -710
Two’s Complement Examples

## Slide 27
Two’s Complement Addition
Add 6 + (-6) using two’s complement numbers
Add -2 + 3 using two’s complement numbers

## Slide 28
Add 6 + (-6) using two’s complement numbers
Add -2 + 3 using two’s complement numbers
Two’s Complement Addition

## Slide 29
Extend number from N to M bits (M > N) :
  Sign-extension
  Zero-extension
Increasing Bit Width

## Slide 30
Sign bit copied to msb’s
Number value is same
Example 1:
  4-bit representation of 3 = 0011
  8-bit sign-extended value: 00000011
Example 2:
  4-bit representation of -5 = 1011
  8-bit sign-extended value: 11111011
Sign-Extension

## Slide 31
Zeros copied to msb’s
Value changes for negative numbers
Example 1:
  4-bit value = 0011 = 310
  8-bit zero-extended value: 00000011 = 310
Example 2:
  4-bit value = 1011 = -510
  8-bit zero-extended value: 00001011 = 1110
Zero-Extension

## Slide 32
Number System | Range
Unsigned | [0, 2N-1]
Sign/Magnitude | [-(2N-1-1), 2N-1-1]
Two’s Complement | [-2N-1, 2N-1-1]
For example, 4-bit representation:
Number System Comparison

## Slide 33
Numbers we can represent using binary representations
  Positive numbers
    Unsigned binary
  Negative numbers
    Two’s complement
    Sign/magnitude numbers
What about fractions?
Number Systems

## Slide 34
Two common notations:
Fixed-point: binary point fixed
Floating-point: binary point floats to the right of the most significant 1
Numbers with Fractions

## Slide 35
6.75 using 4 integer bits and 4 fraction bits:
  Binary point is implied
  The number of integer and fraction bits must be agreed upon beforehand
Fixed-Point Numbers

## Slide 36
Represent 7.510 using 4 integer bits and 4 fraction bits.
  01111000
Fixed-Point Number Example

## Slide 37
Representations:
  Sign/magnitude
  Two’s complement
Example: Represent -7.510 using 4 integer and 4 fraction bits
  Sign/magnitude:
  11111000
  Two’s complement:
  1. +7.5: 01111000
  2. Invert bits: 10000111
  3. Add 1 to lsb: + 1
  10001000
Signed Fixed-Point Numbers

## Slide 38
Binary point floats to the right of the most significant 1
Similar to decimal scientific notation
For example, write 27310 in scientific notation:
  273 = 2.73 × 102
In general, a number is written in scientific notation as:
± M × BE
  M = mantissa
  B = base
  E = exponent
  In the example, M = 2.73, B = 10, and E = 2
Floating-Point Numbers

## Slide 39
Example: represent the value 22810 using a 32-bit floating point representation
We show three versions – final version is called the IEEE 754 floating-point standard
Floating-Point Numbers

## Slide 40
Convert decimal to binary
  22810 = 111001002
Write the number in “binary scientific notation”:
  111001002 = 1.110012 × 27
Fill in each field of the 32-bit floating point number:
  The sign bit is positive (0)
  The 8 exponent bits represent the value 7
  The remaining 23 bits are the mantissa
Floating-Point Representation 1

## Slide 41
First bit of the mantissa is always 1:
  22810 = 111001002 = 1.11001 × 27
So, no need to store it: implicit leading 1
Store just fraction bits in 23-bit field
Floating-Point Representation 2

## Slide 42
Biased exponent: bias = 127 (011111112)
  Biased exponent = bias + exponent
  Exponent of 7 is stored as:
  127 + 7 = 134 = 0x100001102
The IEEE 754 32-bit floating-point representation of 22810
in hexadecimal: 0x43640000
Floating-Point Representation 3

## Slide 43
Write -58.2510 in floating point (IEEE 754)
Floating-Point Example

## Slide 44
Write -58.2510 in floating point (IEEE 754)
Convert decimal to binary:
  58.2510 = 111010.012
Write in binary scientific notation:
1.1101001 × 25
Fill in fields:
  Sign bit: 1 (negative)
  8 exponent bits: (127 + 5) = 132 = 100001002
  23 fraction bits: 110 1001 0000 0000 0000 0000
in hexadecimal: 0xC2690000
Floating-Point Example

## Slide 45
Number | Sign | Exponent | Fraction
0 | X | 00000000 | 00000000000000000000000
∞ | 0 | 11111111 | 00000000000000000000000
- ∞ | 1 | 11111111 | 00000000000000000000000
NaN | X | 11111111 | non-zero
Floating-Point: Special Cases

## Slide 46
Single-Precision:
  32-bit
  1 sign bit, 8 exponent bits, 23 fraction bits
  bias = 127
Double-Precision:
  64-bit
  1 sign bit, 11 exponent bits, 52 fraction bits
  bias = 1023
Floating-Point Precision

## Slide 47
Extract exponent and fraction bits
Prepend leading 1 to form mantissa
Compare exponents
Shift smaller mantissa if necessary
Add mantissas
Normalize mantissa and adjust exponent if necessary
Round result
Assemble exponent and fraction back into floating-point format
Floating-Point Addition

## Slide 48
Add the following floating-point numbers:
0x3FC00000
0x40500000
Floating-Point Addition Example

## Slide 49
1. Extract exponent and fraction bits
For first number (N1): S = 0, E = 127, F = .1
For second number (N2): S = 0, E = 128, F = .101
2. Prepend leading 1 to form mantissa
N1: 1.1
N2: 1.101
Floating-Point Addition Example

## Slide 50
3. Compare exponents
127 – 128 = -1, so shift N1 right by 1 bit
4. Shift smaller mantissa if necessary
shift N1’s mantissa: 1.1 >> 1 = 0.11 (× 21)
5. Add mantissas
0.11 × 21
+ 1.101 × 21
10.011 × 21
Floating-Point Addition Example

## Slide 51
6. Normalize mantissa and adjust exponent if necessary
10.011 × 21 = 1.0011 × 22
7. Round result
No need (fits in 23 bits)
8. Assemble exponent and fraction back into floating-point format
S = 0, E = 2 + 127 = 129 = 100000012, F = 001100..
in hexadecimal: 0x40980000
Floating Point Addition Example

## Slide 52
Perform logic functions:
  inversion (NOT), AND, OR, NAND, NOR, etc.
Single-input:
  NOT gate, buffer
Two-input:
  AND, OR, XOR, NAND, NOR, XNOR
Multiple-input
Logic Gates

## Slide 53
Single-Input Logic Gates

## Slide 54
Two-Input Logic Gates

## Slide 55
More Two-Input Logic Gates

## Slide 56
Multi-input XOR: Odd parity
Multiple-Input Logic Gates

## Slide 57
Discrete voltages represent 1 and 0
For example:
  0 = ground (GND) or 0 volts
  1 = VDD or 5 volts
What about 4.99 volts? Is that a 0 or a 1?
What about 3.2 volts?
Logic Levels

## Slide 58
Range of voltages for 1 and 0
Different ranges for inputs and outputs to allow for noise
Logic Levels

## Slide 59
Anything that degrades the signal
  E.g., resistance, power supply noise, coupling to neighboring wires, etc.
Example: a gate (driver) outputs 5 V but, because of resistance in a long wire, receiver gets 4.5 V
What is Noise?

## Slide 60
With logically valid inputs, every circuit element must produce logically valid outputs
Use limited ranges of voltages to represent discrete values
The Static Discipline

## Slide 61
Noise Margins

## Slide 62
High Noise Margin: NMH = VOH – VIH
Low Noise Margin: NML = VIL – VOL
Noise Margins

## Slide 63
Ideal Buffer: Real Buffer:
NMH = NML = VDD/2
DC Transfer Characteristics
NMH, NML < VDD/2

## Slide 64
DC Transfer Characteristics

## Slide 65
Chapter 1
Digital Design and Computer Architecture: ARM® Edition
Sarah L. Harris and David Money Harris